Department of Electrical and Computer Engineering

Student’s Name:	Calum McConnell
Reporting Week:	Week 6

Tasks outlined in the previous Weekly Progress Report (Provide detailed information on the tasks to be completed this week).
- Assemble Smart speaker PCB
- Test Smart Light successfully
- Research and prep for voice assistant install
Progress made during the reporting week (Provide detailed information on the progress made during the reporting week. Limit your write-up to no more than two page)
Assemble smart speaker PCB
The majority of the components are on the PCB. However, some complications came up; the pinout of the PCB power jack was incorrect, and the potentiometer I selected is too low a resistance for effective use with the DAC. Fixing the jack is simpler, since two pins simply need to be shorted together (the power pin and the pin which is floating when a plug is inserted). While potentiometers of sufficent resistance and the same form factor are readily orderable, it remains to be seen if one is available in-stock somewhere in the various supplies of parts. If not, then an alternative potentiometer can be wired in with longer leads until an order is plaeced for the correct one
Connect smart light consistently / Connect smart door opener
The smart light has yet to be re-connected to the hub; whether the internal bugs persist or not remains to be seen. Similarly, the smart door opener has been encountering bugs on the device (non-hub) side; and debugging will be needed. Various bugs in the connection between pico and computer continue to disrupt and limit progress.
Does your current progress align with the project schedule according to the SMART Goals?
Yes; we are making good progress on a working hub, and the project schedule assumed I would be far less productive this week than last.

Tasks to be completed next week (Outline the tasks to be completed in the upcoming week).
- Documentation on the configuration of the linux system, and setting it up to be transferred to the lab.
- Connection of additional devices
- Smart Speaker assembly complete, research into audio relay over wifi.